## Slide 1: Estimation of Actuation Configuration for a Multi-Actuated Blimp
Semester Thesis
Students: Matthias Krebs Advisors: Kostas Alexis
Simon Laube Markus Achtelik

## Slide 2: Overview
Problem: Motor to Blimp transformation is essential part of controller
Idea: Create blimp model from Motor transformations and fit this model to the system
How: Actuate blimp and compare measurements with model output
Notes: Position of motors is essential for control, but uncertain / unknown

## Slide 3: Concept

## Slide 4: Batch Optimization Process
Actuator Input Pattern .
Model
Optimization Algorithm
Parameters
IMU Data
Model Output
Notes: To optimize the model with respect to the actuation configuration we need to make the model dependent on the actuation configuration.
For a spherical blimp the configuration of an actuator is described with a position on the hull surface and a rotation which tells us in which direction the x axis of the actuator is pointing.
It turns out that this actuator configuration can be expressed with a rotation against the blimps center.
For rotations there are a few parameterisations each of them having advantages and disadvantages
we choose the gibbs-rodriguez and quaternion parameterisation, because gibbs-rodriguez are mini

## Slide 5: Model Function
Thrust force transformation
Thrust force (input)
Angular velocity
Angular acceleration
Radius
Inertia tensor
Parameterization
Gibbs-Rodriguez (3)
Quaternionen (4)
Notes: To optimize the model with respect to the actuation configuration we need to make the model dependent on the actuation configuration.
For a spherical blimp the configuration of an actuator is described with a position on the hull surface and a rotation which tells us in which direction the x axis of the actuator is pointing.
It turns out that this actuator configuration can be expressed with a rotation against the blimps center.
For rotations there are a few parameterisations each of them having advantages and disadvantages. This basically boils down to one trade-off: either you use minimal representation of a rotation and you have to deal with singularities or you use a non-minimal representation and you have to deal with constraints on these parameters.
We decided to use one parameterization which is minimal in the number of parameters and one which does not have the issue of singularities.
we choose the gibbs-rodriguez and quaternion parameterisation, because gibbs-rodriguez are minimal parameters

## Slide 6: Current Results
Gibbs-Rodriguez Parameters
init position
true position
Residual plot in parameter space
Notes: results based on simulator data

## Slide 7: Current Results
Quaternion Parameters
init position
true position
Residual plot in parameter space

## Slide 8: Outlook
Parameterization for radius, inertia tensor
Actuator input patterns
Varied simulation data from modular simulation model
Convergence analysis

## Slide 9: Context / General Description
Control depends on simplified model of blimp
  Fit paramteres of simplified model s.t. it best fits real system

## Slide 10: Problem Formulation
Nonlinear Least Squares Optimization
  : Angular acceleration from gyro measurement : Nonlinear function depending on inputs and parameters
Parametrization
Quaternion
No Singularities
Constrained
Quadratic model
Gibbs-Rodriguez
Singularity at
Unconstrained
Nonlinear model

## Slide 11: Problem Formulation
Quaternion
No Singularities
Constrained
Quadratic model
Gibbs-Rodriguez
Singularity at
Unconstrained
Nonlinear model

## Slide 12: Example
Video?

## Slide 13: Outlook
Inputs bla bla …
Text Cases …
Estimate Accuracy of Result ...