## Slide 1: Estimation of Actuation Configuration for a Multi-Actuated Blimp
Semester Thesis
Students: Matthias Krebs Advisors: Kostas Alexis
Simon Laube Markus Achtelik

## Slide 2: Overview
Problem: Motor to Blimp transformation is essential part of controller
Idea: Create blimp model from Motor transformations and fit this model to the system
How: Actuate blimp and compare measurements with model output
Notes: Position of motors is essential for control, but uncertain / unknown

## Slide 3: Concept

## Slide 4: Batch Optimization Process
Actuator Input Pattern .
Model
Optimization Algorithm
Parameters
IMU Data
Model Output

## Slide 5: Model Function
Thrust force transformation
Thrust force (input)
Angular velocity
Angular acceleration
Radius
Inertia tensor
Parameterization
Gibbs-Rodriguez (3)
Quaternionen (4)
Notes: To optimize the model with respect to the actuation configuration we need to make the model dependent on the actuation configuration.
For a spherical blimp the configuration of an actuator is described with a position on the hull surface and a rotation which tells us in which direction the x axis of the actuator is pointing.
It turns out that this actuator configuration can be expressed with a rotation against the blimps center.
For rotations there are a few parameterisations each of them having advantages and disadvantages. This basically boils down to one trade-off: either you use minimal representation of a rotation and you have to deal with singularities or you use a non-minimal representation and you have to deal with constraints on these parameters.
We decided to use one parameterization which is minimal in the number of parameters and one which does not have the issue of singularities.
we choose the gibbs-rodriguez and quaternion parameterisation, because gibbs-rodriguez are minimal parameters

## Slide 6: Current Results
Iterative parameter optimization (2 actuation units)
init position
true position
Rodriquez
Quaternions
Notes: results based on simulator data

## Slide 7: Current Results
Residual grid plots
Rodriquez
Quaternions

## Slide 8: Outlook
Parameterization for radius, inertia tensor
Actuator input patterns
Varied simulation data from modular simulation model
Convergence analysis